## Slide 1
SATELLITE METEOROLOGY
Part 3: EMR and Instrumentation
Dr. Sam Miller
Professor of Meteorology
Plymouth State University
Open Educational Resource

## Slide 2
BASICS OF EMR

## Slide 3
LIGHT CAN BE DESCRIBED AS A PARTICLE OR A WAVE
Both provide a limited description of light in particular circumstances.
Both are analogies.
Characteristics light manifests depend on the experiment performed.
BASICS OF EMR

## Slide 4
WAVE ANALOGY OF EMR
BASICS OF EMR
Most of the time, the wave analogy is best for use in remote sensing.
Wave characteristics of light include:
Relationship to electrical and magnetic fields
Speed of propagation in a vacuum (c)
Wavelength (l)
Period (T) and frequency (f and w)
Polarization
Phase angle (f)
Doppler shift (Df)
Energy carried by light (DE)
Black body radiation

## Slide 5
WAVE ANALOGY OF EMR
BASICS OF EMR
(Images: Kidder and Vonder Harr, 1995)

## Slide 6
WAVE ANALOGY OF EMR
(Image: Kidder and Vonder Harr, 1995)

## Slide 7
WAVE ANALOGY OF EMR
BASICS OF EMR
(Image: Kidder and Vonder Harr, 1995)
299,792,458

## Slide 8
POLARIZATION
BASICS OF EMR
Polarization refers to the orientation of the electrical field.
May be linear or circular.
If linear, electrical field remains oriented in a fixed plane.
If circular, electrical field rotates around axis of propagation.
(Image: Kidder and Vonder Harr, 1995)

## Slide 9
POLARIZATION
BASICS OF EMR
Polarization refers to the orientation of the electrical field.
May be linear or circular.
If linear, electrical field remains oriented in a fixed plane.
If circular, electrical field rotates around axis of propagation.

## Slide 10
BASICS OF EMR
POLARIZATION

## Slide 11
BASICS OF EMR
POLARIZATION
Right-handed circular polarization rotates clockwise over time

## Slide 12
PHASE ANGLE
BASICS OF EMR
Zero phase angle occurs when the sine wave has a zero value at t = 0

## Slide 13
PHASE ANGLE
BASICS OF EMR
Positive phase angle occurs when the sine wave has a positive value at t = 0

## Slide 14
PHASE ANGLE
BASICS OF EMR
Negative phase angle occurs when the sine wave has a negative value at t = 0

## Slide 15
DOPPLER SHIFT
BASICS OF EMR

## Slide 16
BASICS OF EMR
Frequency shift
Original wavelength of EMR
Velocity of source relative to observer
DOPPLER SHIFT

## Slide 17
BASICS OF EMR
Outbound: Positive Vr
If velocity of source is away from the observer, Vr is a positive number.
This implies a lower frequency (Df < 0).
This also implies a longer observed wavelength: Redshifting
DOPPLER SHIFT

## Slide 18
BASICS OF EMR
If velocity of source is toward the observer, Vr is a negative number.
This implies a higher frequency (Df > 0).
This also implies a shorter observed wavelength: Blueshifting
Inbound: Negative Vr
DOPPLER SHIFT

## Slide 19
From Max Planck: Energy carried by a photon as a function of its wavelength
As wavelength decreases, energy carried by photon increases.
ENERGY CARRIED BY EMR
BASICS OF EMR

## Slide 20
Very high energy
Very low energy
From Max Planck: Energy carried by a photon as a function of its wavelength
As wavelength decreases, energy carried by photon increases.
BASICS OF EMR
ENERGY CARRIED BY EMR
(Image: Kidder and Vonder Harr, 1995)

## Slide 21
PLANCK’S BLACK BODY EQUATION
Describes shape of the black-body function
BASICS OF EMR

## Slide 22
PLANCK’S BLACK BODY EQUATION
Rayleigh-Jeans Approximation
Valid for temperatures and wavelengths in Earth’s atmosphere
BASICS OF EMR

## Slide 23
WIEN’S LAW
BASICS OF EMR

## Slide 24
WIEN’S LAW
As temperature goes up, lmax goes down
BASICS OF EMR
(Image: Kidder and Vonder Harr, 1995)

## Slide 25
WIEN’S LAW
(Image: Kidder and Vonder Harr, 1995)

## Slide 26
STEFAN-BOLTZMANN LAW
BASICS OF EMR

## Slide 27
SOLAR AND TERRESTRIAL SPECTRA
BASICS OF EMR

## Slide 28
SOLAR AND TERRESTRIAL SPECTRA
Both objects are close approximations of black bodies
BASICS OF EMR

## Slide 29
SOLAR AND TERRESTRIAL SPECTRA
Wavelength of maximum emission (brightness) described by Wien’s Law
BASICS OF EMR

## Slide 30
SOLAR AND TERRESTRIAL SPECTRA

## Slide 31
Total amount of energy emitted described by Stefan-Boltzmann Law
SOLAR AND TERRESTRIAL SPECTRA
BASICS OF EMR

## Slide 32
Surface of the Sun is about 20 x hotter than the surface of Earth
Stefan-Boltzmann Law states than Sun emits about 160,000 as much energy per unit area as Earth.
SOLAR AND TERRESTRIAL SPECTRA
BASICS OF EMR

## Slide 33
Sun: About 63,164,000 W/m^2
Earth: About 390 W/m^2
SOLAR AND TERRESTRIAL SPECTRA
BASICS OF EMR

## Slide 34
NON-BLACK BODIES: ALL REAL OBJECTS ARE “GRAY”

## Slide 35
NON-BLACK BODIES: ALL REAL OBJECTS ARE “GRAY”

## Slide 36
NON-BLACK BODIES: ALL REAL OBJECTS ARE “GRAY”
Includes scattering

## Slide 37
NON-BLACK BODIES: ALL REAL OBJECTS ARE “GRAY”
Related to Vertical Optical Depth (more later)

## Slide 38
ADDITIONAL QUANTITIES
BASICS OF EMR

## Slide 39
APPLICATION TO REMOTE SENSING

## Slide 40
The Stefan-Boltzmann Law states that there is a relationship between M and the temperature of a scan spot.
If we can measure M, we’ll have T.
REMOTE SENSING APPLICATIONS
ADDITIONAL QUANTITIES

## Slide 41
RADIANCE AND RADIANT EXITANCE
Scan Spot
The Stefan-Boltzmann Law states that there is a relationship between M and the temperature of a scan spot.
If we can measure M, we’ll have T.
REMOTE SENSING APPLICATIONS

## Slide 42
RADIANCE AND RADIANT EXITANCE
Scan Spot
The Stefan-Boltzmann Law states that there is a relationship between M and the temperature of a scan spot.
If we can measure M, we’ll have T.
REMOTE SENSING APPLICATIONS

## Slide 43
Scan Spot
Circle around Scan Spot with radius = 1
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS

## Slide 44
REMOTE SENSING APPLICATIONS
x
y
z
Scan Spot
Circle around Scan Spot with radius = 1
Rectangular coordinates centered on Scan Spot
RADIANCE AND RADIANT EXITANCE

## Slide 45
REMOTE SENSING APPLICATIONS
x
y
z
Scan Spot
Circle around Scan Spot with radius = 1
Rectangular coordinates centered on Scan Spot
Unit hemisphere over Scan Spot
RADIANCE AND RADIANT EXITANCE
(Image: Kidder and Vonder Harr, 1995)

## Slide 46
Angle f varies from 0 to 2p
(Full circle)
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS
(Image: Kidder and Vonder Harr, 1995)

## Slide 47
Angle f varies from 0 to 2p
(Full circle)
Angle q varies from 0 to p/2
(Quarter circle)
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS
(Image: Kidder and Vonder Harr, 1995)

## Slide 48
Angle f varies from 0 to 2p
(Full circle)
Angle q varies from 0 to p/2
(Quarter circle)
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS
Small area on surface of sphere (dW)
(Image: Kidder and Vonder Harr, 1995)

## Slide 49
Small area on surface of sphere (dW)
Arclength in f direction = Rsinqdf
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS
(Image: Kidder and Vonder Harr, 1995)

## Slide 50
Small area on surface of sphere (dW)
Arclength in f direction = Rsinqdf
Arclength in q direction = Rdq
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS
(Image: Kidder and Vonder Harr, 1995)

## Slide 51
Small area on surface of sphere (dW)
Arclength in f direction = Rsinqdf
Arclength in q direction = Rdq
R=1
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS
(Image: Kidder and Vonder Harr, 1995)

## Slide 52
Small area on surface of sphere:
dW = Rsinqdqdf
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS
(Image: Kidder and Vonder Harr, 1995)

## Slide 53
Small area on surface of sphere:
dW = Rsinqdqdf
This is the ”solid angle.”
Units are Steradians
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS
(Image: Kidder and Vonder Harr, 1995)

## Slide 54
q Is the zenith angle
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS
(Image: Kidder and Vonder Harr, 1995)

## Slide 55
If q is zero, you are looking directly down at the Scan Spot and it is very bright.
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS
(Image: Kidder and Vonder Harr, 1995)

## Slide 56
If q is zero, you are looking directly down at the Scan Spot and it is very bright.
As q increases, the apparent brightness of the Scan Spot decreases.
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS
(Image: Kidder and Vonder Harr, 1995)

## Slide 57
If q is zero, you are looking directly down at the Scan Spot and it is very bright.
As q increases, the apparent brightness of the Scan Spot decreases.
When q reaches 90 degrees, Scan Spot becomes invisible.
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS
(Image: Kidder and Vonder Harr, 1995)

## Slide 58
Conclusion:
For a fixed brightness, the apparent brightness varies with cos q
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS
(Image: Kidder and Vonder Harr, 1995)

## Slide 59
Satellite usually not directly overhead when receiving EMR from the scan spot (q > 0).
RADIANCE AND RADIANT EXITANCE
EMR QUANTITIES
REMOTE SENSING APPLICATIONS

## Slide 60
EMR enters radiometer through “camera eye” called the “Field of View” that has a known solid angle
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS
(Image: Kidder and Vonder Harr, 1995)

## Slide 61
Radiometer does not measure the full Radiant Exitance – only the portion that enters through the Field of View
The is called the Radiance (L)
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS

## Slide 62
If the observed Radiance (L) is summed over the full surface of the unit hemisphere, the total Radiant Exitance (M) can be obtained, and from that, temperature.
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS
(Image: Kidder and Vonder Harr, 1995)

## Slide 63
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS

## Slide 64
This is the Radiance observed through the instrument’s FOV (W m^-2 Sr^-1)
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS

## Slide 65
This term accounts for the variation in apparent brightness with zenith angle
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS

## Slide 66
Remember the small surface area (solid angle) on the surface of the hemisphere
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS

## Slide 67
This sums the Radiance through the circumferental angle f
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS

## Slide 68
This sums the Radiance through the zenith angle q
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS

## Slide 69
Solution:
RADIANCE AND RADIANT EXITANCE
REMOTE SENSING APPLICATIONS

## Slide 70
ABSORPTION AND EMISSION

## Slide 71
SOLAR SPECTRUM AND EQUIVALENT BLACK BODY

## Slide 72
SOLAR SPECTRUM AND EQUIVALENT BLACK BODY
Emission by hot gases

## Slide 73
SOLAR SPECTRUM AND EQUIVALENT BLACK BODY
Absorption by cool gases

## Slide 74
ABSORPTION IN EARTH’S ATMOSPHERE
Ionization
Electron Orbitals
Forbidden
Dissociation
Vibrational
Rotational
ATOMIC
MOLECULAR
ABSORPTION

## Slide 75
ABSORPTION IN EARTH’S ATMOSPHERE
Ionization
Electron Orbitals
Forbidden
Dissociation
Vibrational
Rotational
ATOMIC
MOLECULAR
Degrees of Freedom
ABSORPTION

## Slide 76
ABSORPTION IN EARTH’S ATMOSPHERE
Ionization
Electron Orbitals
Forbidden
Dissociation
Vibrational
Rotational
ATOMIC
MOLECULAR
Very high energy
(Short wavelength)
e.g. Absorption of UV by O3
ABSORPTION

## Slide 77
ABSORPTION IN EARTH’S ATMOSPHERE
Ionization
Electron Orbitals
Forbidden
Dissociation
Vibrational
Rotational
ATOMIC
MOLECULAR
Very low energy
(Long wavelength)
ABSORPTION
e.g. Absorption of IR by CO2, H20

## Slide 78
ABSORPTION IN EARTH’S ATMOSPHERE
Ionization
Electron Orbitals
Forbidden
Dissociation
Vibrational
Rotational
ATOMIC
MOLECULAR
Lowest energy
e.g. Absorption of Microwave by O2
ABSORPTION

## Slide 79
ABSORPTION IN EARTH’S ATMOSPHERE
ABSORPTION
The amount (or efficiency) of absorption (and emission) is parameterized by the Volume Absorption Coefficient
Depends on wavelength

## Slide 80
Gamma and X-ray (“0” - 0.1 mm): Ionization Continuum
ABSORPTION
(Image: Kidder and Vonder Harr, 1995)

## Slide 81
UVC (0.1 - 0.2 mm): Dissociation of O2 molecules into O
UVB (0.2 - 0.3 mm): Dissociation of O3 molecules (Hartley)
UVA (0.3 - 0.4 mm): Quantum interactions in O3 (Higgins)
ABSORPTION
(Image: Kidder and Vonder Harr, 1995)

## Slide 82
Visible (0.4 - 0.7 mm): Dissociation of O3 (Chappuis)
Atmospheric Window
ABSORPTION
(Image: Kidder and Vonder Harr, 1995)

## Slide 83
Visible (0.4 - 0.7 mm): Dissociation of O3 (Chappuis)
Atmospheric Window
Most Solar EMR enters Earth system here
ABSORPTION
(Image: Kidder and Vonder Harr, 1995)

## Slide 84
Near IR (0.7 – 1.0 mm): Vibrational degrees of freedom
O2
H2O
O3
ABSORPTION
(Image: Kidder and Vonder Harr, 1995)

## Slide 85
Middle IR (1.0 – 15 mm): Rotational degrees of freedom
CO
CH4
N2O
O3
CO2
HDO
H2O
Far IR (15 – 1000 mm [1 mm]): Mostly water vapor
(Not shown)
ABSORPTION
(Image: Kidder and Vonder Harr, 1995)

## Slide 86
Middle IR (1.0 – 15 mm): Rotational degrees of freedom
CO
CH4
N2O
O3
CO2
HDO
H2O
Far IR (15 – 1000 mm [1 mm]): Mostly water vapor
(Not shown)
Water Vapor Channels
ABSORPTION
(Image: Kidder and Vonder Harr, 1995)

## Slide 87
Middle IR (1.0 – 15 mm): Rotational degrees of freedom
CO
CH4
N2O
O3
CO2
HDO
H2O
Far IR (15 – 1000 mm [1 mm]): Mostly water vapor
(Not shown)
Atmospheric Window
ABSORPTION
(Image: Kidder and Vonder Harr, 1995)

## Slide 88
Middle IR (1.0 – 15 mm): Rotational degrees of freedom
CO
CH4
N2O
O3
CO2
HDO
H2O
Far IR (15 – 1000 mm [1 mm]): Mostly water vapor
(Not shown)
Atmospheric Window
Most Terrestrial EMR exits Earth system here
ABSORPTION
(Image: Kidder and Vonder Harr, 1995)

## Slide 89
Microwave (1 – 1000 mm): Forbidden reactions
H2O
O2
ABSORPTION
(Image: Kidder and Vonder Harr, 1995)

## Slide 90
Microwave (1 – 1000 mm): Forbidden reactions
H2O
O2
Microwave Sounder
ABSORPTION
(Image: Kidder and Vonder Harr, 1995)

## Slide 91
SCATTERING

## Slide 92
SCATTERING IN EARTH’S ATMOSPHERE
The amount (or efficiency) of scattering is parameterized by the Volume Scattering Coefficient
Depends on wavelength
SCATTERING

## Slide 93
SCATTERING IN EARTH’S ATMOSPHERE
SCATTERING
(Image: Kidder and Vonder Harr, 1995)

## Slide 94
SCATTERING IN EARTH’S ATMOSPHERE
Geometric: Particle >> EMR
Mie: Particle ~= EMR
Rayleigh: Particle << EMR
SCATTERING
(Image: Kidder and Vonder Harr, 1995)

## Slide 95
SCATTERING IN EARTH’S ATMOSPHERE
SCATTERING
Size parameter describes relationship between size of scattering particle and the EMR wavelength
(Image: Kidder and Vonder Harr, 1995)

## Slide 96
Rainbows
SCATTERING IN EARTH’S ATMOSPHERE
SCATTERING
(Image: Kidder and Vonder Harr, 1995)

## Slide 97
Blue Sky
SCATTERING IN EARTH’S ATMOSPHERE
SCATTERING
(Image: Kidder and Vonder Harr, 1995)

## Slide 98
Scattering of IR by clouds
SCATTERING IN EARTH’S ATMOSPHERE
SCATTERING
(Image: Kidder and Vonder Harr, 1995)

## Slide 99
X-Band: 2.5 – 3.7 cm
C-Band: 3.7 – 7.5 cm
S-Band: 7.5 – 15 cm
Basis of Radar Reflectivity
SCATTERING IN EARTH’S ATMOSPHERE
SCATTERING
(Image: Kidder and Vonder Harr, 1995)

## Slide 100
TRANSMITTANCE

## Slide 101
TRANSMITTANCE IN EARTH’S ATMOSPHERE
Transmittance is parameterized by the Volume Extinction Coefficient and Vertical Optical Depth
TRANSMITTANCE
Extinction coefficient is the linear sum of the volume absorption coefficient and the volume scattering coefficient
Depends on wavelength

## Slide 102
TRANSMITTANCE IN EARTH’S ATMOSPHERE
TRANSMITTANCE
Vertical Optical Depth is the vertical integral of the extinction coefficient
Also depends on wavelength
Transmittance is parameterized by the Volume Extinction Coefficient and Vertical Optical Depth

## Slide 103
TRANSMITTANCE IN EARTH’S ATMOSPHERE
TRANSMITTANCE
Vertical Optical Depth is the vertical integral of the extinction coefficient
Also depends on wavelength
Greater extinction (absorption, scattering, or both) implies a greater vertical optical depth
Transmittance is parameterized by the Volume Extinction Coefficient and Vertical Optical Depth

## Slide 104
TRANSMITTANCE IN EARTH’S ATMOSPHERE
TRANSMITTANCE
Relationship of transmittance to vertical optical depth at two levels
Also depends on wavelength
Transmittance is parameterized by the Volume Extinction Coefficient and Vertical Optical Depth

## Slide 105
TRANSMITTANCE IN EARTH’S ATMOSPHERE
TRANSMITTANCE
Relationship of transmittance to vertical optical depth at two levels
Also depends on wavelength
As difference between two Vertical Optical Depths increases, transmittance between those levels decreases
Transmittance is parameterized by the Volume Extinction Coefficient and Vertical Optical Depth

## Slide 106
RADIANCE TRANSFER FUNCTION

## Slide 107
RADIANCE TRANSFER FUNCTION (RTF)
A model of absorption, emission, and scattering in Earth’s atmosphere

## Slide 108
Spacecraft
RADIANCE TRANSFER FUNCTION (RTF)

## Slide 109
SMV
SGT
SSP
Spacecraft
RADIANCE TRANSFER FUNCTION (RTF)

## Slide 110
SMV
SGT
SSP
Spacecraft
RADIANCE TRANSFER FUNCTION (RTF)

## Slide 111
SMV
SGT
SSP
Spacecraft
RADIANCE TRANSFER FUNCTION (RTF)

## Slide 112
Scan line
Spacecraft
RADIANCE TRANSFER FUNCTION (RTF)

## Slide 113
Scan spot
Spacecraft
RADIANCE TRANSFER FUNCTION (RTF)

## Slide 114
Polychromatic radiance
Spacecraft
RADIANCE TRANSFER FUNCTION (RTF)

## Slide 115
Spacecraft
Upwelling radiance
RADIANCE TRANSFER FUNCTION (RTF)

## Slide 116
RADIANCE TRANSFER FUNCTION (RTF)
Spacecraft
Original radiance
Radiance reaching spacecraft
Top of atmosphere
Column of atmosphere

## Slide 117
RADIANCE TRANSFER FUNCTION (RTF)
RTF describes what’s happening here

## Slide 118
RADIANCE TRANSFER FUNCTION (RTF)
Slope describes processes in a small control volume, which are then integrated through the depth of the atmosphere (Ds) to find total change in radiance
y = b + m x

## Slide 119
y = b + m x
RADIANCE TRANSFER FUNCTION (RTF)
Slope includes four terms

## Slide 120
RADIANCE TRANSFER FUNCTION (RTF)
Loss
Gain
Slope includes four terms
y = b + m x

## Slide 121
y = b + m x
RADIANCE TRANSFER FUNCTION (RTF)
Absorption
Emission
Scattering
Slope includes four terms

## Slide 122
y = b + m x
RADIANCE TRANSFER FUNCTION (RTF)
Absorption
Emission
Scattering
Because both absorption/emission and scattering depend on wavelength, all four terms must be evaluated for narrow, monochromatic channels

## Slide 123
RADIANCE TRANSFER FUNCTION (RTF)
Absorption
(Loss)
Volume absorption coefficient
This is a black body term:
The volume absorption coefficient is related to the absorptance (a) at wavelength l
Initial radiance from scan spot entering control volume at wavelength l

## Slide 124
RADIANCE TRANSFER FUNCTION (RTF)
Absorption
(Loss)
Volume absorption coefficient
This is a black body term:
The volume absorption coefficient is related to the absorptance (a) at wavelength l
Initial radiance from scan spot entering control volume at wavelength l
When integrated, this is exponential decay

## Slide 125
RADIANCE TRANSFER FUNCTION (RTF)
Emission
(Gain)
Volume absorption coefficient
This is a black body term:
The volume absorption coefficient is related to the emittance (e) at
wavelength l
Black body emission within the control volume at wavelength l

## Slide 126
RADIANCE TRANSFER FUNCTION (RTF)
Emission
(Gain)
Volume absorption coefficient
This is a black body term:
The volume absorption coefficient is related to the emittance (e) at
wavelength l
Black body emission within the control volume at wavelength l
When integrated, this is exponential growth

## Slide 127
RADIANCE TRANSFER FUNCTION (RTF)
Scattering out
(Loss)
Volume scattering coefficient
This is a white body term:
The volume scattering coefficient is related to the reflectance (r) at
wavelength l
Exponential decay again
Radi
Initial radiance from scan spot entering control volume at wavelength l

## Slide 128
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
Scattering particle

## Slide 129
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
Scattering particle

## Slide 130
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
Initial radiance from scan spot entering control volume at wavelength l
(Ll)

## Slide 131
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
Radiance from somewhere else entering control volume at wavelength l
(L’l)

## Slide 132
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
Encounters scattering particle

## Slide 133
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
Scattered into same direction as initial radiance from scan spot

## Slide 134
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
Imaginary sphere around scattering particle

## Slide 135
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
Imaginary sphere around scattering particle

## Slide 136
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
Radiance from somewhere else (L’l) enters sphere at scattering angle y
Smaller scattering angles more likely to bend L’l into same direction as Ll
y

## Slide 137
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
To account for all possible scattering angles, must integrate around the entire sphere
y

## Slide 138
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
(x,y,z) dimensions
y

## Slide 139
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
f’ is circumferential angle (0 – 2p) Full circle
y

## Slide 140
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
q’ is polar angle (0 – p)
Half circle
y

## Slide 141
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
Volume scattering coefficient

## Slide 142
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
Circumferential angle

## Slide 143
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
Polar angle

## Slide 144
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
Radiance from somewhere else entering sphere at wavelength l as a function of circumferential and polar angle

## Slide 145
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
Weighting function dependent on scattering angle y

## Slide 146
RADIANCE TRANSFER FUNCTION (RTF)
Scattering in
(Gain)
After completing integral on RHS
This is a white body term:
The volume scattering coefficient is related to the reflectance (r) at
wavelength l
Exponential growth again

## Slide 147
RADIANCE TRANSFER FUNCTION (RTF)
Black body
terms
White body
terms
y = b + m x
Now substitute explicit identities into slope term and narrow scope to monochromatic channels

## Slide 148
RADIANCE TRANSFER FUNCTION (RTF)
Black body
terms
White body
terms
Expression becomes:

## Slide 149
RADIANCE TRANSFER FUNCTION (RTF)
Black body
terms
White body
terms
Loss
Expression becomes:

## Slide 150
RADIANCE TRANSFER FUNCTION (RTF)
Black body
terms
White body
terms
Gain
Expression becomes:

## Slide 151
RADIANCE TRANSFER FUNCTION (RTF)
Black body
terms
White body
terms
Or:

## Slide 152
RADIANCE TRANSFER FUNCTION (RTF)
Black body
terms
White body
terms
If no scattering present:
If black body emission within control volume is greater than initial radiance, the radiance reaching satellite is increased
If black body emission within control volume is less than initial radiance, the radiance reaching satellite is decreased

## Slide 153
RADIANCE TRANSFER FUNCTION (RTF)
Black body
terms
White body
terms
If no absorption or emission present:
If radiance from somewhere else scattered into same direction as initial radiance else is greater than initial radiance, the radiance reaching satellite is increased
If radiance from somewhere else scattered into same direction as initial radiance else is less than initial radiance, the radiance reaching satellite is decreased

## Slide 154
PASSIVE SENSORS

## Slide 155
SATELLITE RADIOMETERS
Most satellite instruments are passive sensors
No emission of EMR from instrument
Utilizes environmentally available EMR
Radiometer = quantitative camera
PASSIVE SENSORS

## Slide 156
PASSIVE SENSORS
Specialization of radiometer
Most satellite instruments are passive sensors
No emission of EMR from instrument
Utilizes environmentally available EMR
Radiometer = quantitative camera
IMAGERS
SOUNDERS
SATELLITE RADIOMETERS

## Slide 157
IMAGERS
SATELLITE IMAGERS
Designed to create pictures in narrow range of wavelengths (called channels), one pixel at a time
Specialization of radiometer
IMAGERS

## Slide 158
SATELLITE IMAGERS
IMAGERS
Designed to create pictures in narrow range of wavelengths (called channels), one pixel at a time
Examples:
Advanced Very-High Resolution Radiometer (AVHRR)
[NOAA Polar Orbiters]

## Slide 159
SATELLITE IMAGERS
IMAGERS
Designed to create pictures in narrow range of wavelengths (called channels), one pixel at a time
Examples:
Moderate Resolution Imaging Spectroradiometer (MODIS)
[TERRA/AQUA]

## Slide 160
SATELLITE IMAGERS
IMAGERS
Designed to create pictures in narrow range of wavelengths (called channels), one pixel at a time
Examples:
Visible Infrared Imaging Radiometer Suite (VIIRS)
[JPSS]

## Slide 161
SATELLITE IMAGERS
IMAGERS
Designed to create pictures in narrow range of wavelengths (called channels), one pixel at a time
Examples:
Visible Infrared Imaging Radiometer Suite (VIIRS)
[JPSS]
JPSS

## Slide 162
SATELLITE IMAGERS
IMAGERS
Designed to create pictures in narrow range of wavelengths (called channels), one pixel at a time
Examples:
Advanced Baseline Imager (ABI)
[GOES-R Series]

## Slide 163
SATELLITE IMAGERS
IMAGERS
Designed to create pictures in narrow range of wavelengths (called channels), one pixel at a time
Examples:
Advanced Baseline Imager (ABI)
[GOES-R Series]
GOES-R

## Slide 164
IMAGERS
AVHRR

## Slide 165
IMAGERS
L
AVHRR
SMV
SSP
Limb
Scan Line
Upwelling polychromatic radiance (L)
From scan spot
SGT

## Slide 166
AVHRR
IMAGERS
Field of View (FOV)
L
Upwelling polychromatic (L) radiance enters instrument through the Field of View (FOV)

## Slide 167
AVHRR
IMAGERS
Field of View (FOV)
L
Upwelling polychromatic (L) radiance enters instrument through the Field of View (FOV)
FOV has width of 1300 mradians

## Slide 168
IMAGERS
AVHRR
SMV
Limb
FOV projected to SSP from 850 km creates a scan spot 1.1 km in diameter
Scan Line
SGT

## Slide 169
AVHRR
IMAGERS
Field of View (FOV)
L
Scan Mirror rotates six times per second
Scan Mirror

## Slide 170
IMAGERS
AVHRR
SMV
Limb
Scan Line
SMV carries spacecraft across landscape at 392 km/min, or 6.5 km/sec
SGT

## Slide 171
IMAGERS
AVHRR
SMV
Limb
Scan Line
Scan mirror rotates six times in one second, so successive scan lines are 1.1 km apart
SMV carries spacecraft across landscape at 392 km/min, or 6.5 km/sec
SGT

## Slide 172
AVHRR
IMAGERS
Field of View (FOV)
L
Maximum scan (zenith) angle (q) is 55.3 degrees
Scan Mirror

## Slide 173
IMAGERS
AVHRR
SMV
Limb
Scan Line
q
Scan angle of 55.3 degrees, combined with satellite elevation of 850 km, gives a half-length for scan line of 1230 km
SGT

## Slide 174
IMAGERS
AVHRR
SMV
Limb
Scan Line
Scan angle of 55.3 degrees, combined with satellite elevation of 850 km, gives a half-length for scan line of 1230 km
Full length for scan line is 2460 km
2460 km
SGT
q

## Slide 175
IMAGERS
AVHRR
SMV
Limb
SGT
FOV projected to end of scan line creates scan spot 2.3 km wide in the along-track direction and 6.4 km long in the cross-track direction

## Slide 176
AVHRR
IMAGERS
L
Scan Mirror directs polychromatic radiance into telescope
Scan Mirror
Telescope

## Slide 177
AVHRR
IMAGERS
Types of telescopes?

## Slide 178
AVHRR
IMAGERS
Types of telescopes?
REFRACTING
Polly
Ahoy, etc.
Wooden leg
(not shown)
Note: I tried to find a picture of a monkey holding this telescope

## Slide 179
AVHRR
IMAGERS
Types of telescopes?
REFRACTING
Magnification depends on focal length

## Slide 180
AVHRR
IMAGERS
Types of telescopes?
REFLECTING
Isaac Newton’s reflecting telescope

## Slide 181
AVHRR
IMAGERS
Types of telescopes?
REFLECTING
Hale Telescope on Mount Palomar

## Slide 182
AVHRR
IMAGERS
Types of telescopes?
REFLECTING
Hubble Space Telescope

## Slide 183
AVHRR
IMAGERS
Types of telescopes?
REFLECTING
James Webb Space Telescope

## Slide 184
AVHRR
IMAGERS
Types of telescopes?
REFLECTING
Magnification depends on diameter of primary mirror

## Slide 185
AVHRR
IMAGERS
L
Telescope
Primary Mirror
AVHRR uses a reflecting telescope
(No pirates needed)
Scan Mirror

## Slide 186
AVHRR
IMAGERS
L
Telescope
Primary Mirror
Primary mirror magnifies radiance from FOV and reflects it to secondary mirror
Secondary Mirror
Scan Mirror

## Slide 187
AVHRR
IMAGERS
L
Telescope
Primary Mirror
Secondary mirror focuses radiance through small opening in center of primary mirror
Secondary Mirror
Scan Mirror
L

## Slide 188
AVHRR
IMAGERS
L
Telescope
Primary Mirror
Polychromatic radiance enters splitter that creates six identical beams
Secondary Mirror
Scan Mirror
L
SPLT

## Slide 189
AVHRR
IMAGERS
L
Telescope
Primary Mirror
Polychromatic radiance beams enter color filters
This creates separate monochromatic channels
Secondary Mirror
Scan Mirror
L
FILT
FILT
FILT
FILT
FILT
FILT
Ll
Ll
Ll
Ll
Ll
Ll
Channel 1: 0.58 – 0.68 mm (Visible)
Channel 2: 0.725 – 1.0 mm (IR)
Channel 3a: 1.58 – 1.64 mm (IR)
Channel 3b: 3.55 – 3.93 mm (IR)
Channel 4: 10.3 – 11.3 mm (IR)
Channel 5: 11.5 – 12.5 mm (IR)
SPLT

## Slide 190
AVHRR
IMAGERS
L
Telescope
Primary Mirror
Polychromatic radiance beams enter color filters
This creates separate monochromatic channels
Secondary Mirror
Scan Mirror
L
SPLT
FILT
FILT
FILT
FILT
FILT
FILT
Ll
Ll
Ll
Ll
Ll
Ll
Channel 1: 0.58 – 0.68 mm (Visible)
Channel 2: 0.725 – 1.0 mm (IR)
Channel 3a: 1.58 – 1.64 mm (IR)
Channel 3b: 3.55 – 3.93 mm (IR)
Channel 4: 10.3 – 11.3 mm (IR)
Channel 5: 11.5 – 12.5 mm (IR)
Weak O3 dissociation (atmospheric window)
Vibrational transitions of O3 and H2O
Rotational transitions of H2O
Rotational transitions of HDO
Weak rotational transitions of CO2 (atmospheric window)
Weak rotational transitions of CO2 and H2O
Absorption/emission processes in these channels

## Slide 191
AVHRR
IMAGERS
L
Telescope
Primary Mirror
Monochromatic radiance beams enter photo-cells that generate a continuous electric signal proportional to the brightness in the channel
Secondary Mirror
Scan Mirror
L
SPLT
FILT
FILT
FILT
FILT
FILT
FILT
Ll
Ll
Ll
Ll
Ll
Ll
PV
PV
PV
PV
PV
PV
~
~
~
~
~
~

## Slide 192
AVHRR
IMAGERS
L
Telescope
Primary Mirror
Analog-to-Digital (A2D) sampling of each channel occurs once each 25 msec
Secondary Mirror
Scan Mirror
L
SPLT
FILT
FILT
FILT
FILT
FILT
FILT
Ll
Ll
Ll
Ll
Ll
Ll
PV
PV
PV
PV
PV
PV
~
~
~
~
~
~
A2D
A2D
A2D
A2D
A2D
A2D

## Slide 193
IMAGERS
AVHRR
SMV
Limb
SGT
In 25 msec, the scan mirror rotates through 942 mradians of arc

## Slide 194
IMAGERS
AVHRR
SMV
Limb
SGT
In 25 msec, the scan mirror rotates through 942 mradians of arc
Combined with the satellite elevation of 850 km, this puts the centroids of the scan spots 800 meters apart near the subsatellite point

## Slide 195
AVHRR
IMAGERS
L
Telescope
Primary Mirror
Digital voltages are encoded as 10-bit binary
Secondary Mirror
Scan Mirror
L
SPLT
FILT
FILT
FILT
FILT
FILT
FILT
Ll
Ll
Ll
Ll
Ll
Ll
PV
PV
PV
PV
PV
PV
~
~
~
~
~
~
A2D
A2D
A2D
A2D
A2D
A2D

## Slide 196
AVHRR
IMAGERS
L
Telescope
Primary Mirror
Digital voltages are encoded as 10-bit binary
Secondary Mirror
Scan Mirror
L
SPLT
FILT
FILT
FILT
FILT
FILT
FILT
Ll
Ll
Ll
Ll
Ll
Ll
PV
PV
PV
PV
PV
PV
~
~
~
~
~
~
A2D
A2D
A2D
A2D
A2D
A2D
There are 1024 possible different brightness levels (0 – 1023)

## Slide 197
AVHRR
IMAGERS
L
Telescope
Primary Mirror
Binary brightness values are stored to flash memory
Secondary Mirror
Scan Mirror
L
SPLT
FILT
FILT
FILT
FILT
FILT
FILT
Ll
Ll
Ll
Ll
Ll
Ll
PV
PV
PV
PV
PV
PV
~
~
~
~
~
~
A2D
A2D
A2D
A2D
A2D
A2D
Memory

## Slide 198
IMAGERS
AVHRR
SMV
Limb
SGT
There are 2048 scan spots in each scan line

## Slide 199
IMAGERS
AVHRR
SMV
Limb
SGT
There are 2048 scan spots in each scan line
AVHRR completes six scan lines every second

## Slide 200
IMAGERS
AVHRR
SMV
Limb
SGT
There are 2048 scan spots in each scan line
AVHRR completes six scan lines every second
Each scan spot radiance is recorded by six channels

## Slide 201
IMAGERS
AVHRR
SMV
Limb
SGT
There are 2048 scan spots in each scan line
AVHRR completes six scan lines every second
Each scan spot radiance is recorded by six channels
Total number of radiances recorded = 73,728 per second

## Slide 202
IMAGERS
AVHRR
Factors limiting resolution of instrument
Mirror rotation rate and SMV: Sets along-track distance between adjacent scan lines = 1.09 km
Mirror rotation rate and A2D conversion rate: Sets cross-track distance between scan spot centroids = 800 meters at SSP
FOV and satellite elevation: Sets minimum size of each scan spot = 1.1 km circle at SSP
Result: Best resolution is about 1.1 km at SSP

## Slide 203
IMAGERS
AVHRR
Data downloading
High-Resolution Picture Transmission (HRPT): Full resolution, all channels. 5.25 W transmitter on spacecraft.
Automatic Picture Transmission (APT): Reduced resolution, channels 1 and 4 only. 5 W transmitter on spacecraft.

## Slide 204
IMAGERS
AVHRR
Data downloading
High-Resolution Picture Transmission (HRPT): Full resolution, all channels. 5.25 W transmitter on spacecraft.
Automatic Picture Transmission (APT): Reduced resolution, channels 1 and 4 only. 5 W transmitter on spacecraft.
Three ground stations for receiving HRPT:
NOAA Command and Data Acquisition (CDA) stations at Gilmore Creek, Alaska and Wallops Island, Virginia
European Centre d’Etudes Spatiales (CNES) in France
All data then transferred to NOAA Satellite Operations Center (NSOC) in Suitland, Maryland

## Slide 205
MODIS CHANNELS
IMAGERS
NASA TERRA & AQUA

## Slide 206
MODIS CHANNELS
IMAGERS
NASA TERRA & AQUA
36 Channels
Visible

## Slide 207
MODIS CHANNELS
IMAGERS
NASA TERRA & AQUA
36 Channels
IR

## Slide 208
VIIRS CHANNELS
IMAGERS
NOAA JPSS

## Slide 209
VIIRS CHANNELS
IMAGERS
NOAA JPSS
22 Channels
Visible

## Slide 210
VIIRS CHANNELS
IMAGERS
NOAA JPSS
22 Channels
IR

## Slide 211
ABI CHANNELS
IMAGERS
NOAA GOES
(Schmit et al., 2017)

## Slide 212
ABI CHANNELS
IMAGERS
NOAA GOES
16 Channels
Visible
(Schmit et al., 2017)

## Slide 213
ABI CHANNELS
IMAGERS
NOAA GOES
16 Channels
IR
(Schmit et al., 2017)

## Slide 214
ABI CHANNELS
IMAGERS
NOAA GOES
16 Channels
IR - WV
(Schmit et al., 2017)

## Slide 215
ENHANCEMENT CURVES
Polychromatic (all channels)
IMAGERS

## Slide 216
Polychromatic (all channels)
Monochromatic (one channel)
ENHANCEMENT CURVES
IMAGERS

## Slide 217
Polychromatic (all channels)
Monochromatic (one channel)
For AVHRR, Radiance reported in each channel is encoded in 10-bit binary (1024 possible brightness levels)
Reduced to 256 brightness levels, and for IR is inverted: Bright white = cold; black = warm
ENHANCEMENT CURVES
IMAGERS

## Slide 218
Unenhanced radiances and corresponding temperatures
ENHANCEMENT CURVES
IMAGERS
(Image: Kidder and Vonder Harr, 1995)

## Slide 219
Unenhanced radiances and corresponding temperatures
Brightness levels
ENHANCEMENT CURVES
IMAGERS
(Image: Kidder and Vonder Harr, 1995)

## Slide 220
Unenhanced radiances and corresponding temperatures
Temperature scale
ENHANCEMENT CURVES
IMAGERS
(Image: Kidder and Vonder Harr, 1995)

## Slide 221
Unenhanced radiances and corresponding temperatures
Black = Warm
White = Cold
ENHANCEMENT CURVES
IMAGERS
(Image: Kidder and Vonder Harr, 1995)

## Slide 222
Unenhanced radiances and corresponding temperatures
These temperatures outside meteorologically meaningful range
ENHANCEMENT CURVES
IMAGERS
(Image: Kidder and Vonder Harr, 1995)

## Slide 223
General purpose enhancement curve
“Zeroes out” unnecessary gray-scale; uses remaining brightness level to increase resolution at low and high-end temperatures
Greater slope = better resolution
ENHANCEMENT CURVES
IMAGERS
(Image: Kidder and Vonder Harr, 1995)

## Slide 224
General purpose enhancement curve
ENHANCEMENT CURVES
IMAGERS
ZA Curve

## Slide 225
Other enhancement curves (legacy)
ENHANCEMENT CURVES
IMAGERS
MB Curve for cold thunderstorms tops
(Image: Kidder and Vonder Harr, 1995)

## Slide 226
Other enhancement curves (legacy)
ENHANCEMENT CURVES
IMAGERS
BD Curve for hurricanes
(Image: Kidder and Vonder Harr, 1995)

## Slide 227
Other enhancement curves (legacy)
ENHANCEMENT CURVES
IMAGERS
MB Curve

## Slide 228
Other enhancement curves (legacy)
ENHANCEMENT CURVES
IMAGERS
BD Curve

## Slide 229
Other enhancement curves
ENHANCEMENT CURVES
IMAGERS

## Slide 230
Other enhancement curves (modern)
ENHANCEMENT CURVES
IMAGERS
National Hurricane Center (NHC) enhancement of IR image
Colors are coded by cloud-top temperature

## Slide 231
ENHANCEMENT CURVES
IMAGERS
Other enhancement curves (modern)
Enhanced water vapor image
Curve emphasizes dry and moist areas

## Slide 232
ATMOSPHERIC SOUNDERS
SOUNDERS
Specialization of radiometer
SOUNDERS

## Slide 233
ATMOSPHERIC SOUNDERS
Key Idea (1959): “If the atmosphere is observed at carefully chosen wavelengths, it is possible to retrieve the Planck Radiance, and therefore the temperature, as a function of height.”
SOUNDERS
Specialization of radiometer
SOUNDERS

## Slide 234
ATMOSPHERIC SOUNDERS
Two broad classes of sounders:
Active: LIDAR and Radar
Passive: Environmental radiance is used
Key Idea (1959): “If the atmosphere is observed at carefully chosen wavelengths, it is possible to retrieve the Planck Radiance, and therefore the temperature, as a function of height.”
SOUNDERS

## Slide 235
ATMOSPHERIC SOUNDERS
Two broad classes of sounders:
Active: LIDAR and Radar
Passive: Environmental radiance is used
Vertical: Radiance coming from atmosphere below satellite is sensed.
Limb: Radiance from limb of atmosphere is sensed.
Key Idea (1959): “If the atmosphere is observed at carefully chosen wavelengths, it is possible to retrieve the Planck Radiance, and therefore the temperature, as a function of height.”
SOUNDERS

## Slide 236
ATMOSPHERIC SOUNDERS
Two broad classes of sounders:
Active: LIDAR and Radar
Passive: Environmental radiance is used
Vertical: Radiance coming from atmosphere below satellite is sensed.
Limb: Radiance from limb of atmosphere is sensed.
Key Idea (1959): “If the atmosphere is observed at carefully chosen wavelengths, it is possible to retrieve the Planck Radiance, and therefore the temperature, as a function of height.”
SOUNDERS

## Slide 237
SLANT RANGE OPTICAL DEPTH
Recall definition of Vertical Optical Depth:
SOUNDERS

## Slide 238
Spacecraft
Upwelling radiance
SLANT RANGE OPTICAL DEPTH
SSP
SOUNDERS

## Slide 239
Spacecraft
Upwelling radiance
SSP
SLANT RANGE OPTICAL DEPTH
SOUNDERS

## Slide 240
Spacecraft
SLANT RANGE OPTICAL DEPTH
SOUNDERS

## Slide 241
Spacecraft
Integral limits of Vertical Optical Depth
z1
z2
SLANT RANGE OPTICAL DEPTH
SOUNDERS
Okay when looking at the SSP

## Slide 242
z1
z2
Spacecraft
Integral limits of Vertical Optical Depth
SLANT RANGE OPTICAL DEPTH
SOUNDERS
When viewing down the scan line, need Slant Range Optical Depth

## Slide 243
sl1
sl2
Spacecraft
Integral limits of Slant Range Optical Depth
SLANT RANGE OPTICAL DEPTH
SOUNDERS

## Slide 244
sl1
sl2
Spacecraft
q
Zenith angle
Let m = cos q
SLANT RANGE OPTICAL DEPTH
SOUNDERS

## Slide 245
sl1
sl2
Spacecraft
q
Zenith angle
Relationship between Vertical Optical Depth and Slant Range Optical Depth:
SLANT RANGE OPTICAL DEPTH
SOUNDERS

## Slide 246
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)
Definitions: Absorption Number and Single-Scatter Albedo
SOUNDERS

## Slide 247
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)
RTF Becomes:
SOUNDERS

## Slide 248
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)
RTF Becomes:
Initial Radiance from Scan Spot
SOUNDERS

## Slide 249
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)
RTF Becomes:
Gain from emission within atmosphere
SOUNDERS

## Slide 250
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)
RTF Becomes:
Gain from scattering into same direction as initial radiance
SOUNDERS

## Slide 251
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)
If no scattering:
Schwarzchild Equation:
Basis of Atmospheric Sounders
SOUNDERS

## Slide 252
Schwarzchild Equation:
Basis of Atmospheric Sounders
(This is the RTF with no scattering.)
SOUNDERS
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)

## Slide 253
SOUNDERS
After solving for radiance reaching the satellite:
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)

## Slide 254
SOUNDERS
After solving for radiance reaching the satellite:
Surface Term (Noise)
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)

## Slide 255
SOUNDERS
After solving for radiance reaching the satellite:
Sky Term (Noise)
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)

## Slide 256
SOUNDERS
After solving for radiance reaching the satellite:
Atmospheric Term
This is the contribution to the total radiance from emission within the column of air between the surface and the satellite.
If we can determine the black-body radiance between h0 and hT (base and top of a layer), we can determine the temperature.
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)

## Slide 257
SOUNDERS
After solving for radiance reaching the satellite:
Atmospheric Term
Weighting functions determine where the radiance is coming from.
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)

## Slide 258
Solving for weighting function between h0 (surface) and hT (centroid of weight):
SOUNDERS
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)

## Slide 259
SOUNDERS
Weight is dependent on zenith angle
Weight is dependent on elevation
Solving for weighting function between h0 (surface) and hT (centroid of weight):
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)

## Slide 260
Surface Term (Noise) = f(transmittance)
Sky Term (Noise) = f(transmittance)
Atmospheric Component
SOUNDERS
Solving for weighting function between h0 (surface) and hT (centroid of weight):
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)

## Slide 261
Surface Term (Noise) = f(transmittance)
Sky Term (Noise) = f(transmittance)
Atmospheric Component
Conclusion: Choose transmittance, and you choose the shape of the weight and therefore where (at what depth in the atmosphere) most of the radiance comes from.
SOUNDERS
Solving for weighting function between h0 (surface) and hT (centroid of weight):
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)

## Slide 262
Chain of logic linking wavelength to the shape of the weighting function:
SOUNDERS
1. Weights are a function of transmittance;
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)

## Slide 263
Chain of logic linking wavelength to the shape of the weighting function:
SOUNDERS
Weights are a function of transmittance;
Transmittance is a function of Vertical Optical Depth;
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)

## Slide 264
Chain of logic linking wavelength to the shape of the weighting function:
SOUNDERS
Weights are a function of transmittance;
Transmittance is a function of Vertical Optical Depth;
Vertical Optical Depth is a function of the extinction coefficient;
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)

## Slide 265
Chain of logic linking wavelength to the shape of the weighting function:
SOUNDERS
Weights are a function of transmittance;
Transmittance is a function of Vertical Optical Depth;
Vertical Optical Depth is a function of the extinction coefficient;
Extinction coefficient is a function of the volume
absorption coefficient and the volume scattering
coefficient;
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)

## Slide 266
Chain of logic linking wavelength to the shape of the weighting function:
SOUNDERS
Weights are a function of transmittance;
Transmittance is a function of Vertical Optical Depth;
Vertical Optical Depth is a function of the extinction coefficient;
Extinction coefficient is a function of the volume
absorption coefficient and the volume scattering
coefficient;
Volume absorption and scattering coefficients are
both functions of wavelength.
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)

## Slide 267
Chain of logic linking wavelength to the shape of the weighting function:
SOUNDERS
Weights are a function of transmittance;
Transmittance is a function of Vertical Optical Depth;
Vertical Optical Depth is a function of the extinction coefficient;
Extinction coefficient is a function of the volume
absorption coefficient and the volume scattering
coefficient;
Volume absorption and scattering coefficients are
both functions of wavelength.
Choose the wavelength and you choose the weights.
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)

## Slide 268
SOUNDERS
RECALL:
Microwave (1 – 1000 mm): Forbidden reactions
H2O
O2
Microwave Sounder
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)
(Image: Kidder and Vonder Harr, 1995)

## Slide 269
SOUNDERS
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)
(Image: Kidder and Vonder Harr, 1995)

## Slide 270
SOUNDERS
Very small difference in wavelength within this absorption peak results in large difference in height of weight centroid
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)
(Image: Kidder and Vonder Harr, 1995)

## Slide 271
SOUNDERS
Variation of weights with wavelength and zenith angle
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)
(Image: Kidder and Vonder Harr, 1995)

## Slide 272
SOUNDERS
Variation of weights with wavelength and zenith angle
Vertical Scales
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)
(Image: Kidder and Vonder Harr, 1995)

## Slide 273
SOUNDERS
Variation of weights with wavelength and zenith angle
Magnitude of Weights
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)
(Image: Kidder and Vonder Harr, 1995)

## Slide 274
SOUNDERS
Variation of weights with wavelength and zenith angle
Channels
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)
(Image: Kidder and Vonder Harr, 1995)

## Slide 275
SOUNDERS
Variation of weights with wavelength and zenith angle
Sample height of weight centroid (hT)
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)
(Image: Kidder and Vonder Harr, 1995)

## Slide 276
SOUNDERS
Variation of weights with wavelength and zenith angle
55.45 GHz (0.541 cm)
53.85 GHz (0.557 cm)
52.85 GHz (0.5676 cm)
Wavelength dependency:
As l increases, hT decreases
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)
(Image: Kidder and Vonder Harr, 1995)

## Slide 277
SOUNDERS
Variation of weights with wavelength and zenith angle
55.45 GHz (0.541 cm)
53.85 GHz (0.557 cm)
52.85 GHz (0.5676 cm)
Zenith angle dependency:
As q increases, hT increases
IMPROVED RADIANCE TRANSFER FUNCTION (RTF)
(Image: Kidder and Vonder Harr, 1995)

## Slide 278
ATMOSPHERIC SOUNDERS
SOUNDERS
Designed to generate vertical profiles of temperature and water vapor mixing ratio. Also used to generate either profiles or vertically-integrated values of other variables, such as O3 concentration.

## Slide 279
ATMOSPHERIC SOUNDERS
SOUNDERS
Designed to generate vertical profiles of temperature and water vapor mixing ratio. Also used to generate either profiles or vertically-integrated values of other variables, such as O3 concentration.
Examples:
High-Resolution Infra-Red Sounder (HIRS)
[NOAA Polar Orbiters]

## Slide 280
ATMOSPHERIC SOUNDERS
SOUNDERS
Designed to generate vertical profiles of temperature and water vapor mixing ratio. Also used to generate either profiles or vertically-integrated values of other variables, such as O3 concentration.
Examples:
Advanced Microwave Sounding Unit – A1 (AMSU-A1)
[NOAA Polar Orbiters]

## Slide 281
ATMOSPHERIC SOUNDERS
SOUNDERS
Designed to generate vertical profiles of temperature and water vapor mixing ratio. Also used to generate either profiles or vertically-integrated values of other variables, such as O3 concentration.
Examples:
Cross-Track Infrared Sounder (CrIS)
[JPSS]

## Slide 282
ATMOSPHERIC SOUNDERS
SOUNDERS
Designed to generate vertical profiles of temperature and water vapor mixing ratio. Also used to generate either profiles or vertically-integrated values of other variables, such as O3 concentration.
Examples:
JPSS
Cross-Track Infrared Sounder (CrIS)
[JPSS]

## Slide 283
ATMOSPHERIC SOUNDERS
SOUNDERS
Designed to generate vertical profiles of temperature and water vapor mixing ratio. Also used to generate either profiles or vertically-integrated values of other variables, such as O3 concentration.
Examples:
Advanced Technology Microwave Sounder (ATMS)
[JPSS]

## Slide 284
ATMOSPHERIC SOUNDERS
SOUNDERS
Designed to generate vertical profiles of temperature and water vapor mixing ratio. Also used to generate either profiles or vertically-integrated values of other variables, such as O3 concentration.
Examples:
JPSS
Advanced Technology Microwave Sounder (ATMS)
[JPSS]

## Slide 285
SOUNDERS
Operation similar to imagers
ATMOSPHERIC SOUNDERS

## Slide 286
SOUNDERS
Operation similar to imagers
ATMOSPHERIC SOUNDERS
Uses a scan mirror to direct telescope to several scan spots along a scan line

## Slide 287
SOUNDERS
Operation similar to imagers
ATMOSPHERIC SOUNDERS
Uses a scan mirror to direct telescope to several scan spots along a scan line
More channels than an imager

## Slide 288
SOUNDERS
Channels are selected using a color wheel
Color wheel from James Webb Space Telescope
ATMOSPHERIC SOUNDERS
Instead of multiple sensors, a single sensor looks at a scan spot while the color wheel is rotated to obtain radiances in different channels

## Slide 289
SOUNDERS
Channels are selected using a color wheel
Scan spots are larger and there are fewer of them in each scan line
ATMOSPHERIC SOUNDERS

## Slide 290
SOUNDERS
Channels are selected using a color wheel
Scan spots are larger and there are fewer of them in each scan line
ATMOSPHERIC SOUNDERS
There are fewer scan lines completed each second

## Slide 291
HIRS CHANNELS
SOUNDERS
NASA POES
20 Channels

## Slide 292
HIRS CHANNELS
SOUNDERS
NASA POES
20 Channels

## Slide 293
AMSU CHANNELS
SOUNDERS
NASA POES
15 Channels

## Slide 294
AMSU CHANNELS
SOUNDERS
NASA POES
15 Channels

## Slide 295
CrIS CHANNELS
SOUNDERS
JPSS
2,211 Channels

## Slide 296
ATMS CHANNELS
SOUNDERS
JPSS
22 Channels

## Slide 297
ATMS CHANNELS
SOUNDERS
JPSS
22 Channels

## Slide 298
MODIS CHANNELS
NASA TERRA & AQUA
SOUNDERS
With 36 channels, MODIS functions as both an imager and a sounder

## Slide 299
THE GOES ABI IS ALSO A SOUNDER
SOUNDERS
(Schmit et al., 2017)

## Slide 300
THE GOES ABI IS ALSO A SOUNDER
SOUNDERS
(Schmit et al., 2017)

## Slide 301
THE GOES ABI IS ALSO A SOUNDER
SOUNDERS
(Schmit et al., 2017)
ABI LEGACY VERTICAL TEMPERATURE DATA CAN BE OBTAINED AT:
https://www.ncei.noaa.gov/access/metadata/landing-page/bin/iso?id=gov.noaa.ncdc:C01513

## Slide 302
SOUNDING RETRIEVALS
SOUNDERS
Question to be answered: What portion of the radiance in each of the sounder’s channels came from the black-body temperature of the atmosphere, and what portion came from trace gas emission?

## Slide 303
SOUNDING RETRIEVALS
SOUNDERS
Question to be answered: What portion of the radiance in each of the sounder’s channels came from the black-body temperature of the atmosphere, and what portion came from trace gas emission?
Water vapor is one of the trace gases.

## Slide 304
SOUNDING RETRIEVALS
SOUNDERS
Question to be answered: What portion of the radiance in each of the sounder’s channels came from the black-body temperature of the atmosphere, and what portion came from trace gas emission?
Idea: Use channels that are free of trace gas emission to determine the temperature. Remainder of the radiance should be due to trace gas emission.
Water vapor is one of the trace gases.

## Slide 305
SOUNDING RETRIEVALS
SOUNDERS
Question to be answered: What portion of the radiance in each of the sounder’s channels came from the black-body temperature of the atmosphere, and what portion came from trace gas emission?
Idea: Use channels that are free of trace gas emission to determine the temperature. Remainder of the radiance should be due to trace gas emission.
Water vapor is one of the trace gases.
Problem: There are no channels free of trace gas emission.

## Slide 306
SOUNDING RETRIEVALS
SOUNDERS
Question to be answered: What portion of the radiance in each of the sounder’s channels came from the black-body temperature of the atmosphere, and what portion came from trace gas emission?
Idea: Use channels that are free of trace gas emission to determine the temperature. Remainder of the radiance should be due to trace gas emission.
Water vapor is one of the trace gases.
Problem: There are no channels free of trace gas emission.
So, we are left with the original problem.

## Slide 307
SOUNDING RETRIEVALS
SOUNDERS
Question to be answered: What portion of the radiance in each of the sounder’s channels came from the black-body temperature of the atmosphere, and what portion came from trace gas emission?
Problem is further compounded by the fact that satellite radiance measurements are not discrete (the weighting functions of the channels overlap).

## Slide 308
SOUNDING RETRIEVALS
SOUNDERS
Question to be answered: What portion of the radiance in each of the sounder’s channels came from the black-body temperature of the atmosphere, and what portion came from trace gas emission?
Problem is further compounded by the fact that satellite radiance measurements are not discrete (the weighting functions of the channels overlap).
This is why we need “retrieval methods.”

## Slide 309
SOUNDING RETRIEVALS
SOUNDERS
Question to be answered: What portion of the radiance in each of the sounder’s channels came from the black-body temperature of the atmosphere, and what portion came from trace gas emission?
RETRIEVAL METHODS
PHYSICAL
STATISTICAL
HYBRID

## Slide 310
SOUNDING RETRIEVALS
SOUNDERS
PHYSICAL RETRIEVALS
Can be used for either temperature or water vapor mixing ratio

## Slide 311
SOUNDING RETRIEVALS
SOUNDERS
PHYSICAL RETRIEVALS
CALCULATE FIRST-GUESS CURRENT TEMPERATURE PROFILE
Possible sources of First Guess Profile:
Climatology
Nearby radiosonde
Forecast sounding from models
Black-Body Temperature

## Slide 312
SOUNDING RETRIEVALS
SOUNDERS
PHYSICAL RETRIEVALS
CALCULATE FIRST-GUESS CURRENT TEMPERATURE PROFILE
CALCULATE RADIANCES EXPECTED IN EACH CHANNEL FROM CURRENT PROFILE
Black-Body Temperature
These are black-body radiances computed by using the RTF
Requires knowledge of transmittance (t)

## Slide 313
SOUNDING RETRIEVALS
SOUNDERS
PHYSICAL RETRIEVALS
CALCULATE FIRST-GUESS CURRENT TEMPERATURE PROFILE
CALCULATE RADIANCES EXPECTED IN EACH CHANNEL FROM CURRENT PROFILE
COMPARE OBSERVED RADIANCES TO COMPUTED RADIANCES
Black-Body Temperature
This is where the observed radiances from the satellite sounder come into the process

## Slide 314
SOUNDING RETRIEVALS
SOUNDERS
PHYSICAL RETRIEVALS
CALCULATE FIRST-GUESS CURRENT TEMPERATURE PROFILE
CALCULATE RADIANCES EXPECTED IN EACH CHANNEL FROM CURRENT PROFILE
COMPARE OBSERVED RADIANCES TO COMPUTED RADIANCES
WITHIN DE?
Black-Body Temperature
The amount of precision required determines the number of cycles through the loop

## Slide 315
SOUNDING RETRIEVALS
SOUNDERS
PHYSICAL RETRIEVALS
CALCULATE FIRST-GUESS CURRENT TEMPERATURE PROFILE
CALCULATE RADIANCES EXPECTED IN EACH CHANNEL FROM CURRENT PROFILE
COMPARE OBSERVED RADIANCES TO COMPUTED RADIANCES
WITHIN DE?
NO
ADJUST CURRENT TEMPERATURE PROFILE
Black-Body Temperature
Cycle back if not within tolerance.
Repeat as many times as necessary.

## Slide 316
SOUNDING RETRIEVALS
SOUNDERS
PHYSICAL RETRIEVALS
CALCULATE FIRST-GUESS CURRENT TEMPERATURE PROFILE
CALCULATE RADIANCES EXPECTED IN EACH CHANNEL FROM CURRENT PROFILE
COMPARE OBSERVED RADIANCES TO COMPUTED RADIANCES
WITHIN DE?
YES
ACCEPT PROFILE
Black-Body Temperature
Stop when error is acceptable.

## Slide 317
SOUNDING RETRIEVALS
SOUNDERS
PHYSICAL RETRIEVALS
Advantages:
Physical processes clearly evident at each stage
No large database of coincident radiosonde data is necessary
Disadvantages:
Computationally intensive
Requires knowledge of transmittance (t)
Does not utilize known statistical properties of atmosphere

## Slide 318
SOUNDING RETRIEVALS
SOUNDERS
STATISTICAL RETRIEVALS
ASSUME THAT SOUNDER CHANNELS CORRECTLY SAMPLE THE ATMOSPHERE AT DIFFERENT LEVELS

## Slide 319
SOUNDING RETRIEVALS
SOUNDERS
STATISTICAL RETRIEVALS
ASSUME THAT SOUNDER CHANNELS CORRECTLY SAMPLE THE ATMOSPHERE AT DIFFERENT LEVELS
CORRELATE CHANNEL RADIANCES TO NEARBY SOUNDING IN TRAINING DATA SET
Training Data Set consists of large number of observed temperature and moisture profiles.

## Slide 320
SOUNDING RETRIEVALS
SOUNDERS
STATISTICAL RETRIEVALS
ASSUME THAT SOUNDER CHANNELS CORRECTLY SAMPLE THE ATMOSPHERE AT DIFFERENT LEVELS
CORRELATE CHANNEL RADIANCES TO NEARBY SOUNDING IN TRAINING DATA SET
Training Data Set consists of large number of observed temperature and moisture profiles.
Must be large to assure mathematical stability, and should contain soundings over varied surface types and latitude zones.

## Slide 321
SOUNDING RETRIEVALS
SOUNDERS
STATISTICAL RETRIEVALS
ASSUME THAT SOUNDER CHANNELS CORRECTLY SAMPLE THE ATMOSPHERE AT DIFFERENT LEVELS
CORRELATE CHANNEL RADIANCES TO NEARBY SOUNDING IN TRAINING DATA SET
Training Data Set consists of large number of observed temperature and moisture profiles.
Must be large to assure mathematical stability, and should contain soundings over varied surface types and latitude zones.
Must be recent and updated frequently.

## Slide 322
SOUNDING RETRIEVALS
SOUNDERS
STATISTICAL RETRIEVALS
ASSUME THAT SOUNDER CHANNELS CORRECTLY SAMPLE THE ATMOSPHERE AT DIFFERENT LEVELS
CORRELATE CHANNEL RADIANCES TO NEARBY SOUNDING IN TRAINING DATA SET
Training Data Set consists of large number of observed temperature and moisture profiles.
Must be large to assure mathematical stability, and should contain soundings over varied surface types and latitude zones.
Must be recent and updated frequently.
Correlations must be done separately for each satellite to account for small differences in instrument calibration.

## Slide 323
SOUNDING RETRIEVALS
SOUNDERS
STATISTICAL RETRIEVALS
ASSUME THAT SOUNDER CHANNELS CORRECTLY SAMPLE THE ATMOSPHERE AT DIFFERENT LEVELS
CORRELATE CHANNEL RADIANCES TO NEARBY SOUNDING IN TRAINING DATA SET
Training Data Set consists of large number of observed temperature and moisture profiles.
RTF is not used. Does not require knowledge of transmittance (t)
Must be large to assure mathematical stability, and should contain soundings over varied surface types and latitude zones.
Must be recent and updated frequently.
Correlations must be done separately for each satellite to account for small differences in instrument calibration.

## Slide 324
SOUNDING RETRIEVALS
SOUNDERS
STATISTICAL RETRIEVALS
ASSUME THAT SOUNDER CHANNELS CORRECTLY SAMPLE THE ATMOSPHERE AT DIFFERENT LEVELS
CORRELATE CHANNEL RADIANCES TO NEARBY SOUNDING IN TRAINING DATA SET
APPLY STATISTICAL RELATIONSHIP TO LOCATIONS WITHOUT IN SITU DATA

## Slide 325
SOUNDING RETRIEVALS
SOUNDERS
Advantages:
Much less computationally intensive than physical retrievals
Does not require knowledge of transmittance or use of the RTF
Extensively utilizes known statistical properties of the atmosphere
Disadvantages:
Training Data Set should include radiosonde profiles from mountain tops and the ocean (rare)
Radiosondes launched at 00Z and 12Z; hard to obtain “recent” soundings
STATISTICAL RETRIEVALS

## Slide 326
SOUNDING RETRIEVALS
SOUNDERS
HYBRID RETRIEVALS
Mathematically similar to statistical retrievals
Uses Weighting Functions (as in physical retrievals) but does not involve numerical integration of the RTF
Main advantage: Easier to put into operation that either of the other two
Main disadvantage: Requires knowledge of transmittance

## Slide 327
SOUNDING RETRIEVALS
SOUNDERS
HYBRID RETRIEVALS
Mathematically similar to statistical retrievals
Uses Weighting Functions (as in physical retrievals) but does not involve numerical integration of the RTF
Main advantage: Easier to put into operation that either of the other two
Main disadvantage: Requires knowledge of transmittance
This is the way it’s done operationally.

## Slide 328
OPERATIONAL SOUNDING RETRIEVALS
SOUNDERS
PREPROCESSOR
Receives infra-red and microwave sounder(s) binary from Satellite Operations Control Center (SOCC), Office of Satellite and Product Operations (OSPO); Performs initial QA/QC
Earth-locate each scan spot
Convert binary data points to radiances
Correct radiances for water vapor absorption
Make initial guess for surface albedo and skin temperature
Apply albedo corrections to daytime data
Apply limb corrections (make all data equivalent to nadir)
Correct data from microwave sounders for side lobes
Interpolate data from different sensors onto a common grid
ADVANCED TIROS OPERATIONAL VERTICAL SOUNDER (ATOVS)

## Slide 329
ADVANCED TIROS OPERATIONAL VERTICAL SOUNDER (ATOVS)
OPERATIONAL SOUNDING RETRIEVALS
SOUNDERS
PREPROCESSOR
ATMOSPHERIC RADIANCE MODULE
Delivers spatially-averaged clear-column radiances to retrieval module; outputs a single set of radiances from an ensemble of scan spots
SGT
7 along-track
9 cross-track
TOTAL: 63 Scan Spots

## Slide 330
ADVANCED TIROS OPERATIONAL VERTICAL SOUNDER (ATOVS)
OPERATIONAL SOUNDING RETRIEVALS
SOUNDERS
PREPROCESSOR
ATMOSPHERIC RADIANCE MODULE
Delivers spatially-averaged clear-column radiances to retrieval module; outputs a single set of radiances from an ensemble of scan spots
All 63 scan spots tested for cloud contamination using IR sounder’s visible channel
If at least 4 are uncontaminated, uses weighted average of radiances from the IR sounder
If 1 – 3 are uncontaminated, uses combination of IR and microwave sounder radiances
If none are uncontaminated, uses microwave sounder radiances only

## Slide 331
ADVANCED TIROS OPERATIONAL VERTICAL SOUNDER (ATOVS)
OPERATIONAL SOUNDING RETRIEVALS
SOUNDERS
PREPROCESSOR
ATMOSPHERIC RADIANCE MODULE
Delivers spatially-averaged clear-column radiances to retrieval module; outputs a single set of radiances from an ensemble of scan spots
Some applications are using 3 x 3 (9 spot) ensemble for higher resolution output

## Slide 332
ADVANCED TIROS OPERATIONAL VERTICAL SOUNDER (ATOVS)
OPERATIONAL SOUNDING RETRIEVALS
SOUNDERS
PREPROCESSOR
ATMOSPHERIC RADIANCE MODULE
RETRIEVAL MODULE
Performs sounding retrieval using ensemble averaged clear-column radiances.
Uses hybrid retrieval method.
Data are archived by National Environmental Satellite Data and Information Service (NESDIS):
Temperature and dew point, virtual temperature, Integrated Precipitable Water (IPW), tropopause height and pressure, total ozone, others.

## Slide 333
SOUNDERS
Overlapping weights means radiance from a given height is used in more than one channel
EVALUATION OF QUALITY OF SOUNDER DATA

## Slide 334
SOUNDERS
Overlapping weights means radiance from a given height is used in more than one channel
Acts like a low-pass filter: Fine details are smoothed out (lost)
EVALUATION OF QUALITY OF SOUNDER DATA

## Slide 335
SOUNDERS
Comparison of GOES VAS-derived vertical profiles to profiles obtained using radiosondes
VAS = Visible and Infrared Spin Scan Radiometer (VISSR) Atmospheric Sounder
TOVS = TIROS Operational Vertical Sounder
EVALUATION OF QUALITY OF SOUNDER DATA
(Image: Kidder and Vonder Harr, 1995)

## Slide 336
Comparison of GOES VAS-derived vertical profiles to profiles obtained using radiosondes
VAS = Visible and Infrared Spin Scan Radiometer (VISSR) Atmospheric Sounder
TOVS = TIROS Operational Vertical Sounder
SOUNDERS
Weights associated with each channel
EVALUATION OF QUALITY OF SOUNDER DATA
(Image: Kidder and Vonder Harr, 1995)

## Slide 337
SOUNDERS
VAS misses fine details near surface and tropopause
Dew point profile is worse than temperature profile
EVALUATION OF QUALITY OF SOUNDER DATA
(Image: Kidder and Vonder Harr, 1995)
Comparison of GOES VAS-derived vertical profiles to profiles obtained using radiosondes
VAS = Visible and Infrared Spin Scan Radiometer (VISSR) Atmospheric Sounder
TOVS = TIROS Operational Vertical Sounder

## Slide 338
SOUNDERS
EVALUATION OF QUALITY OF SOUNDER DATA
Radiosonde profiles – Nationwide Eclipse Ballooning Project
(Picciano 2024)
Objective of project: Evaluate changes to atmosphere during a total solar eclipse.
Nationwide project funded by NASA
Involved 17 atmospheric sites
Picciano (2024) compared ABI legacy temperature profiles to radiosonde data

## Slide 339
SOUNDERS
EVALUATION OF QUALITY OF SOUNDER DATA
Radiosonde profiles – Nationwide Eclipse Ballooning Project
(Picciano 2024)
Objective of project: Evaluate changes to atmosphere during a total solar eclipse.
Nationwide project funded by NASA
Involved 17 atmospheric sites
Picciano (2024) compared ABI legacy temperature profiles to radiosonde data
THREE COMPARISON SITES

## Slide 340
SOUNDERS
EVALUATION OF QUALITY OF SOUNDER DATA
Radiosonde profiles – Nationwide Eclipse Ballooning Project
(Picciano 2024)
ATOVS = Advanced TIROS Operational Vertical Sounder
Converts radiances from ABI channels into vertical profiles of T and Td
Note: No microwave channels in ABI; infrared only
THREE COMPARISON SITES

## Slide 341
SOUNDERS
EVALUATION OF QUALITY OF SOUNDER DATA
(Picciano 2024)
Comparison of GOES-E ABI Legacy Vertical Temperature Profiles from ATOVS to radiosonde data

## Slide 342
SOUNDERS
Comparison of GOES-E ABI Legacy Vertical Temperature Profiles from ATOVS to radiosonde data
EVALUATION OF QUALITY OF SOUNDER DATA
(Picciano 2024)

## Slide 343
SOUNDERS
EVALUATION OF QUALITY OF SOUNDER DATA
(Picciano 2024)
Comparison of GOES-E ABI Legacy Vertical Temperature Profiles from ATOVS to radiosonde data

## Slide 344
SOUNDERS
EVALUATION OF QUALITY OF SOUNDER DATA
(Picciano 2024)
Comparison of GOES-E ABI Legacy Vertical Temperature Profiles from ATOVS to radiosonde data
(Values shown in Kelvins)
N = 19

## Slide 345
SOUNDERS
EVALUATION OF QUALITY OF SOUNDER DATA
(Picciano 2024)
Comparison of GOES-E ABI Legacy Vertical Temperature Profiles from ATOVS to radiosonde data
(Values shown in Kelvins)
N = 19
WORST RESULTS NEAR SFC AND TROPOPAUSE

## Slide 346
SOUNDERS
EVALUATION OF QUALITY OF SOUNDER DATA
(Picciano 2024)
Comparison of GOES-E ABI Legacy Vertical Temperature Profiles from ATOVS to radiosonde data
(Values shown in Kelvins)
N = 19
BEST RESULTS IN MIDDLE TROPOSPHERE

## Slide 347
EVALUATION OF QUALITY OF SOUNDER DATA
SOUNDERS
Work by Gruber and Watkins (1982) found:
RMS difference between satellite and radiosonde temperature profiles is smaller than natural variability in mid-latitudes.
RMS differences are greatest near surface and tropopause, where temperature and water vapor mixing ratio lapse rates vary sharply with height.
Bias (satellite – radiosonde) small for clear soundings (IR sounder); larger for cloudy soundings (microwave sounder)
Temperatures in troughs too warm; in ridges too cool.

## Slide 348
ACTIVE SENSORS

## Slide 349
ACTIVE SENSORS
ACTIVE SENSORS
Emit either pulses or continuous wave of EMR
Usually operate in microwave region of spectrum (radar)
EMR interacts with target and is scattered back to radiometer

## Slide 350
ACTIVE SENSORS
ACTIVE SENSORS
Poseidon 3B Radar Altimeter
[TOPEX/Poseidon and Jason Polar Orbiters]
Examples:
Purpose: Sea-surface elevation

## Slide 351
ACTIVE SENSORS
ACTIVE SENSORS
Examples:
Poseidon 3B Radar Altimeter
[TOPEX/Poseidon and Jason Polar Orbiters]

## Slide 352
ACTIVE SENSORS
ACTIVE SENSORS
Advanced Scatterometer (ASCAT)
[METOP ESA Polar Orbiter]
Examples:
Purpose: Sea-surface winds

## Slide 353
ACTIVE SENSORS
ACTIVE SENSORS
Examples:
Advanced Scatterometer (ASCAT)
[METOP ESA Polar Orbiter]

## Slide 354
ACTIVE SENSORS
ACTIVE SENSORS
Examples:
Advanced Scatterometer (ASCAT)
[METOP ESA Polar Orbiter]
Sea surface wind speeds from a research paper (Kumar et al. 2021)

## Slide 355
ACTIVE SENSORS
ACTIVE SENSORS
Examples:
Advanced Scatterometer (ASCAT)
[METOP ESA Polar Orbiter]
Sea surface wind vectors from a research paper (Cohen 2023)

## Slide 356
ACTIVE SENSORS
ACTIVE SENSORS
Examples:
Advanced Scatterometer (ASCAT)
[METOP ESA Polar Orbiter]
Sea surface wind vectors from a research paper (Cohen 2023)

## Slide 357
ACTIVE SENSORS
ACTIVE SENSORS
Examples:
Seasat-A Satellite Scatterometer (SASS)
[Seasat Polar Orbiter]
Purpose: Sea-surface winds

## Slide 358
ACTIVE SENSORS
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
Extensive series of aircraft studies in the 1960s indicated a relationship between sea-surface winds and radar returns from the sea surface

## Slide 359
ACTIVE SENSORS
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
Extensive series of aircraft studies in the 1960s indicated a relationship between sea-surface winds and radar returns from the sea surface
NASA developed a specialized radar called a scatterometer
Measures backscatter cross-section (proportional to returned power) per unit area

## Slide 360
ACTIVE SENSORS
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
Extensive series of aircraft studies in the 1960s indicated a relationship between sea-surface winds and radar returns from the sea surface
NASA developed a specialized radar called a scatterometer
Measures backscatter cross-section (proportional to returned power) per unit area
s = normalized radar cross-section

## Slide 361
ACTIVE SENSORS
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS

## Slide 362
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
ACTIVE SENSORS

## Slide 363
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
ACTIVE SENSORS

## Slide 364
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
ACTIVE SENSORS
This is solvable!

## Slide 365
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
ACTIVE SENSORS
Sensor transmits pulses of microwave energy (radar) at sea surface from polar orbit
f = 14.6 GHz, or l = 2.05 cm; transmitted power is about 8 Watts
Interacts with capillary waves on sea surface via Bragg Scattering
Greatest backscatter in upwind and downwind direction (sees face of approaching waves or backs of departing waves)
Smallest backscatter in cross-wind direction (see sides of waves)
Seasat-A Satellite Scatterometer (SASS)
[Seasat Polar Orbiter]

## Slide 366
Seasat-A Satellite Scatterometer (SASS)
[Seasat Polar Orbiter]
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
ACTIVE SENSORS
Sensor transmits pulses of microwave energy (radar) at sea surface from polar orbit
f = 14.6 GHz, or l = 2.05 cm; transmitted power is about 8 Watts
Interacts with capillary waves on sea surface via Bragg Scattering
Greatest backscatter in upwind and downwind direction (sees face of approaching or departing waves)
Smallest backscatter in cross-wind direction (see sides of waves)
About the same size as radar waves
Defined as: “…small, free, surface-water wave with such a short wavelength that its restoring force is the water's surface tension, which causes the wave to have a rounded crest and V-shaped trough.”

## Slide 367
Seasat-A Satellite Scatterometer (SASS)
[Seasat Polar Orbiter]
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
ACTIVE SENSORS
Sensor transmits pulses of microwave energy (radar) at sea surface from polar orbit
f = 14.6 GHz, or l = 2.05 cm; transmitted power is about 8 Watts
Interacts with capillary waves on sea surface via Bragg Scattering
Greatest backscatter in upwind and downwind direction (sees face of approaching or departing waves)
Smallest backscatter in cross-wind direction (see sides of waves)
About the same size as radar waves
Defined as: “…small, free, surface-water wave with such a short wavelength that its restoring force is the water's surface tension, which causes the wave to have a rounded crest and V-shaped trough.”

## Slide 368
Seasat-A Satellite Scatterometer (SASS)
[Seasat Polar Orbiter]
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
ACTIVE SENSORS
Sensor transmits pulses of microwave energy (radar) at sea surface from polar orbit
f = 14.6 GHz, or l = 2.05 cm; transmitted power is about 8 Watts
Interacts with capillary waves on sea surface via Bragg Scattering
Greatest backscatter in upwind and downwind direction (sees face of approaching or departing waves)
Smallest backscatter in cross-wind direction (see sides of waves)
About the same size as radar waves
Defined as: “…small, free, surface-water wave with such a short wavelength that its restoring force is the water's surface tension, which causes the wave to have a rounded crest and V-shaped trough.”
Capillary waves on sea surface

## Slide 369
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
ACTIVE SENSORS
Sensor transmits pulses of microwave energy (radar) at sea surface from polar orbit
f = 14.6 GHz, or l = 2.05 cm; transmitted power is about 8 Watts
Interacts with capillary waves on sea surface via Bragg Scattering
Greatest backscatter in upwind and downwind direction (sees face of approaching or departing waves)
Smallest backscatter in cross-wind direction (see sides of waves)
Seasat-A Satellite Scatterometer (SASS)
[Seasat Polar Orbiter]

## Slide 370
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
ACTIVE SENSORS
Sensor transmits pulses of microwave energy (radar) at sea surface from polar orbit
f = 14.6 GHz, or l = 2.05 cm; transmitted power is about 8 Watts
Interacts with capillary waves on sea surface via Bragg Scattering
Greatest backscatter in upwind and downwind direction (sees face of approaching or departing waves)
Smallest backscatter in cross-wind direction (see sides of waves)

## Slide 371
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
ACTIVE SENSORS
Sensor transmits pulses of microwave energy (radar) at sea surface from polar orbit
f = 14.6 GHz, or l = 2.05 cm; transmitted power is about 8 Watts
Interacts with capillary waves on sea surface via Bragg Scattering
Greatest backscatter in upwind and downwind direction (sees face of approaching or departing waves)
Smallest backscatter in cross-wind direction (see sides of waves)
EMR from Scatterometer

## Slide 372
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
ACTIVE SENSORS
Sensor transmits pulses of microwave energy (radar) at sea surface from polar orbit
f = 14.6 GHz, or l = 2.05 cm; transmitted power is about 8 Watts
Interacts with capillary waves on sea surface via Bragg Scattering
Greatest backscatter in upwind and downwind direction (sees face of approaching or departing waves)
Smallest backscatter in cross-wind direction (see sides of waves)
EMR from Scatterometer
Compliment of zenith angle

## Slide 373
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
ACTIVE SENSORS
Sensor transmits pulses of microwave energy (radar) at sea surface from polar orbit
f = 14.6 GHz, or l = 2.05 cm; transmitted power is about 8 Watts
Interacts with capillary waves on sea surface via Bragg Scattering
Greatest backscatter in upwind and downwind direction (sees face of approaching or departing waves)
Smallest backscatter in cross-wind direction (see sides of waves)
EMR from Scatterometer
Compliment of zenith angle
Wave height of capillary waves

## Slide 374
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
ACTIVE SENSORS
Sensor transmits pulses of microwave energy (radar) at sea surface from polar orbit
f = 14.6 GHz, or l = 2.05 cm; transmitted power is about 8 Watts
Interacts with capillary waves on sea surface via Bragg Scattering
Greatest backscatter in upwind and downwind direction (sees face of approaching or departing waves)
Smallest backscatter in cross-wind direction (see sides of waves)
EMR from Scatterometer
Compliment of zenith angle
Wave height of capillary waves
Bragg Scattering given by:

## Slide 375
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
ACTIVE SENSORS
Sensor transmits pulses of microwave energy (radar) at sea surface from polar orbit
f = 14.6 GHz, or l = 2.05 cm; transmitted power is about 8 Watts
Interacts with capillary waves on sea surface via Bragg Scattering
Greatest backscatter in upwind and downwind direction (sees face of approaching or departing waves)
Smallest backscatter in cross-wind direction (see sides of waves)
EMR from Scatterometer
Compliment of zenith angle
Wave height of capillary waves
Bragg Scattering given by:
Wavelength of EMR

## Slide 376
How do scatterometers measure sea-surface winds?
ACTIVE SENSORS
ACTIVE SENSORS
Sensor transmits pulses of microwave energy (radar) at sea surface from polar orbit
f = 14.6 GHz, or l = 2.05 cm; transmitted power is about 8 Watts
Interacts with capillary waves on sea surface via Bragg Scattering
Greatest backscatter in upwind and downwind direction (sees face of approaching or departing waves)
Smallest backscatter in cross-wind direction (see sides of waves)
EMR from Scatterometer
Compliment of zenith angle
Wave height of capillary waves
Bragg Scattering given by:
Order number of intensity maxima (= 1, 2, 3…)

## Slide 377
ACTIVE SENSORS
SEASAT-A SATELLITE SCATTEROMETER
Seasat-A Satellite Scatterometer (SASS)
[Seasat Polar Orbiter]
Need two measurements of back-scatter cross-section to back out wind speed and direction

## Slide 378
ACTIVE SENSORS
SEASAT-A SATELLITE SCATTEROMETER
Spacecraft
Seasat-A Satellite Scatterometer (SASS)
[Seasat Polar Orbiter]
Need two measurements of back-scatter cross-section to back out wind speed and direction

## Slide 379
SEASAT-A SATELLITE SCATTEROMETER
Spacecraft
SMV
ACTIVE SENSORS
CROSS-TRACK
ALONG-TRACK

## Slide 380
SEASAT-A SATELLITE SCATTEROMETER
Spacecraft
SMV
ACTIVE SENSORS
1350 KM
SCAN LINES ARE ABOUT HALF AS WIDE AS THAT OF AVHRR

## Slide 381
SEASAT-A SATELLITE SCATTEROMETER
Spacecraft
SMV
ACTIVE SENSORS
SCAN LINE 45 DEGREES AHEAD OF SSP
~3 MINUTES
SCAN LINE 45 DEGREES BEHIND SSP
INSTRUMENT IMAGES SAME LOCATIONS ON THE OCEAN SURFACE TWICE: ONCE AS IT APPROACHES, AND ONCE AS IT DEPARTS

## Slide 382
SEASAT-A SATELLITE SCATTEROMETER
SMV
ACTIVE SENSORS
Center Swath
Left Swath
Right Swath
Spacecraft
~3 MINUTES
SCAN LINES ARE SEPARATED INTO THREE SWATHS

## Slide 383
SEASAT-A SATELLITE SCATTEROMETER
SMV
ACTIVE SENSORS
Spacecraft
SCAN SPOTS
~3 MINUTES
INTERSECTIONS OF SWATHS AND SCAN LINES ARE SCAN SPOTS
RADAR BEAMS

## Slide 384
SEASAT-A SATELLITE SCATTEROMETER
SMV
ACTIVE SENSORS
Spacecraft
s2
s2
s2
s1
s1
s1
~3 MINUTES
SCAN SPOTS
TWO VALUES OF s ARE OBTAINED FOR EACH SCAN SPOT, THREE MINUTES APART
RADAR BEAMS

## Slide 385
SEASAT-A SATELLITE SCATTEROMETER
SMV
ACTIVE SENSORS
Spacecraft
s2
s1
~3 MINUTES

## Slide 386
SEASAT-A SATELLITE SCATTEROMETER
ACTIVE SENSORS

## Slide 387
SEASAT-A SATELLITE SCATTEROMETER
ACTIVE SENSORS
Scan direction as spacecraft is approaching scan spot
s1
OCEAN WAVE CRESTS

## Slide 388
SEASAT-A SATELLITE SCATTEROMETER
ACTIVE SENSORS
Scan direction as spacecraft is departing from scan spot
s2
OCEAN WAVE CRESTS

## Slide 389
SEASAT-A SATELLITE SCATTEROMETER
ACTIVE SENSORS
Seen from above
OCEAN WAVE CRESTS
SCAN AS SPACECRAFT APPROACHES
SCAN AS SPACECRAFT DEPARTS
WAVE PROPAGATION
y1
y2 = y1 + 90
~3 MINUTES

## Slide 390
SEASAT-A SATELLITE SCATTEROMETER
SMV
ACTIVE SENSORS
Spacecraft
s2
s2
s2
s1
s1
s1
~3 MINUTES
SCAN SPOTS
RADAR BEAMS
With two measurements we can solve the system of equations and obtain wind vector data for each scan spot on the scan line.

## Slide 391
SUMMARY

## Slide 392
SUMMARY
Light (EMR) can be described as a particle or a wave.
For most remote sensing applications, the wave analogy is appropriate.
It is combination of an electrical and a magnetic wave with a specific wavelength (l).
Additional properties are polarization and phase angle.
Energy carried by EMR is inversely proportional to l.
Remember black, white, and clear bodies.
Planck’s Law, Wien’s Law, and Stefan-Boltzmann Law
Black-body emission and trace gas emission
Radiant Flux Density (M) and Radiance (L)
Absorption, emission, scattering, and transmittance
Radiance Transfer Function and four terms
Extinction and vertical optical depth
Schwarzchild equation (RTF without scattering)
EMR THEORY

## Slide 393
SUMMARY
Radiometers
Passive sensors
Imagers (e.g. AVHRR, ABI)
Enhancement curves
Factors limiting resolution
Sounders (e.g. HIRS, ATMS)
Weights – Centroids determined by choice of l
Sounding retrieval methods – TOVS/ATOVS
Active sensors (e.g. ASCAT, SASS) – sea-surface winds
Low-power radar (microwave)
INSTRUMENTATION

## Slide 394
References
Cohen, L., 2023: Satellite Verification of the NHC Designation of the 17 January 2023 NW Atlantic Cyclone, term paper for Satellite Meteorology (MT5330), Plymouth State University, 27 pp.
Kidder, S.Q., and T.H. Vonder Harr, 1995: Satellite Meteorology – An Introduction, San Diego: Academic Press, 466 pgs. (PRIMARY SOURCE)
Picciano, G., 2024: A Comparison of Atmospheric Profile Retrieval Methods From the 8 April 2024 Total Solar Eclipse, Semester Project in Satellite Meteorology (MT5330), Plymouth State University.
Schmit, T., P. Griffith, M. Gunshor, J. Daniels, S. Goodman, and W. Lebair, 2017: A closer look at the ABI on the GOES-R series, Bulletin of the American Meteorological Society, 98 (4), pp. 681 – 698, https://doi.org/10.1175/BAMS-D-15-00230.1
Public domain sources